ODAS (Ocean Data Acquisition System) Metadata Format Version 1.1

(Draft)

ODAS metadata is the information about Ocean Data Acquisition Systems. ODAS Metadata Format Recommendation 1 (JCOMM-I) were developed by the Subgroup on Marine Climatology to describe the data from such ocean data acquisition systems as moored and drifting buoys, profile floats, offshore platform and so on. They focus on the descriptions of original features of observing data, especially the environmental features in data acquisition.

ODAS metadata format has two levels. Level 1 is the header records which describe the general information and acquisition conditions of dataset sources. Level 2 is the detailed descriptions of working conditions of various sensors. A sensor record will only exist when there is an actual sensor on the platform and it can be repeated for every sensor of a given type. ODAS metadata record structure sees Figure 1.

At the JCOMM DMCG-I meeting in 2002, the National Marine Data and Information Service (NMDIS) of China volunteered to undertake the construction of the ODAS Metadata Management Center. NMDIS perfected the ODAS Metadata Format Recommendation 1 to draft the ODAS Metadata Format Version 1.1. Latest location date and location of platforms were added in the header record (HR). The platform ID in ODAS was added in both header record and sensor records to link platform and its sensors. Code table was extended.

ODAS XML Schema has been developed and used by ODAS Metadata Management Center. They are compatible with the ODAS metadata format 1.1. Annex 1 is ODAS tables for ODAS metadata content, annex 2 is XML schema for ODAS metadata format 1.1.

Figure 1.  ODAS metadata record structure

Annex 1: ODAS metadata content

# HEADER RECORD

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | ID |  | Platform ID in ODAS, keyword, can’t repeat |
| 2 | mc |  | Metadata contributor, abbreviation name of organization or DAC that contribute metadata |
| 3 | ts |  | Type of station |
|  |  | MB | Moored buoy |
|  |  | DB | Drifting buoy |
|  |  | ID | Ice drifter |
|  |  | FP | Fixed platform (oil rig, etc.) |
|  |  | IS | Island station |
|  |  | AL | Automatic light station |
|  |  | CM | Coastal marine automated station |
|  |  | PF | Profiling floats (e.g. ARGO — a global array of profiling floats) |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 1 Header record) |
| 4 | WMOn |  | WMO number — 5-digit identifier |
| 5 | stn |  | Unique call sign if available; otherwise, station name (C-MAN, platforms, etc.) |
| 6 | AIn |  | Additional identifier number; define in footnote # 2 (e.g. ARGOS = up to 7 digits, GOES no., others) |
| 7 | ind |  | Period of validity/beginning of historical record (initiation date, e.g. 1995-3-21) date of mooring, launching, or platform instrumentation (date the platform began collecting weather observations under its current ID and location). If the platform is moved or assigned a new ID then a new period of validity should be initiated. |
| 8 | oed |  | Operational end date of platform operations (e.g. 2000-1-27). This item is associated with the entry above which shows the beginning date and this item the ending date when a platform closed operations. If for example a moored buoy was placed in the Great Lakes each spring and withdrawn each winter the beginning date would not change unless the identifier, ownership, or location changed at some point. When one of these change, a new beginning date should be entered “ind” above and an operational end date entered in this field |
| 9 | ltd |  | Latest location date of platform. |
| 10 | cnty | see list | Country of ownership — International Organization for Standardization |
| 11 | ragy |  | Responsible agency/organization within a country responsible for the platform’s operations, launch, and metadata [e.g. in the United States it could be the National Ocean Service (NOS) NOAA, National Data Buoy Center (NDBC) NOAA, Woods Hole Institute, etc.] List the full name of the organization or agency responsible. |
| 12 | ldmu |  | Last date metadata updated (e.g. 2000-5-27) |
| 13 | DA |  | Degree of automation |
|  |  | 1 | Fully automated |
|  |  | 2 | Always supplemented with manual input |
|  |  | 3 | Occasionally supplemented with manual input |
|  |  | 4 | Fully manual (no automation) |
|  |  | 5 | Unknown |
| 14 | Lat |  | Latitude — degrees, up to three decimal places if available (e.g. 50.985 N/S) |
| 15 | Lon |  | Longitude — degrees, up to three decimal places if available (e.g. 124.976 E/W) |
| 16 | ltlat |  | Latest latitude, up to three decimal places, the value is from –90 to 90, southern latitude is negative value and northern latitude is positive value. |
| 17 | ltlon |  | Latest longitude, up to three decimal places, the value is from –180 to 180, western longitude is negative value and eastern longitude is positive value. |
| 18 | WC |  | Watch circle — nearest whole metre (e.g. 346.5 = 347 m). The maximum distance a moored buoy can be located from its central position related to the length and type of mooring. Outside the watch circle and the moored buoy is likely adrift |
| 19 | lngth |  | Length — the length of the platform (if rectangular or boat shape hull). See code “diam” below if the platform is a discus. Metres to tenths (e.g. 26.9 m) |
| 20 | Brth |  | Breath — the breadth (width) of the platform (if rectangular or boat shaped hull). Metres to tenths (e.g. 12.6 m) |
| 21 | Diam |  | Diameter — platform dimension for discus type hulls. Diameter in metres to tenths (e.g. 6.0 m) |
| 22 | Hult |  | Hull type |
|  |  | DS | Discus (cylinders) |
|  |  | BS | Boat shaped hull |
|  |  | RS | Rectangular shape |
|  |  | SP | Spars |
|  |  | OD | ODAS 30 series |
|  |  | NM | NOMAD |
|  |  | TR | Torus |
|  |  | CN | Conic |
|  |  | OR | Omnidirectional wave-rider |
|  |  | DR | Directional wave-rider |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 3 Header record) |
| 23 | Huln |  | Hull or platform number — enter as assigned (a combination of numeric and alpha characters if required) |
| 24 | Mtyp |  | Mooring type — mooring type if a moored buoy or drogue type if drifting buoy |
|  |  | AC | All chain (shallow depths generally up to 90 m) |
|  |  | ST | Semitaut (intermediated depths generally 60 to 600 m — generally nylon cable) |
|  |  | FC | Float inverse catenary (deep ocean generally 600 to 6 000 m — generally nylon with glass floats) |
|  |  | PC | Poly-nylon inverse catenary (deep ocean generally 1 200 to 6 000 m) |
|  |  | DT | Drogue type |
|  |  | HS | Holey sock drogue |
|  |  | TS | Tristar |
|  |  | WS | Window shade |
|  |  | PA | Parachute |
|  |  | NL | Non-Lagrangian sea anchor Use for either mooring or drogue as needed |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 4 Header record) |
| 25 | Cmsy |  | Satellite data-collection system — system used to transmit the observations |
|  |  | GO | GOES DCP |
|  |  | AR | ARGOS PTT |
|  |  | GA | GOES primary ARGOS backup |
|  |  | RF | RF |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 5 Header record) |
| 26 | Stt |  | Satellite transmission time — time slot assigned for observation transmission. Hours and minutes UTC (e.g. 1230) or for example, on the hour, on the half-hour, two orbits per day, etc. |
| 27 | Foo |  | Frequency of observations — hours and minutes (e.g. every hour = 1.0, every 6 hours = 6.0, or every half hour 0.5, etc., I = irregular) |
| 28 | dfmt |  | Data format — data format (Manual on Codes (WMO-No. 306)) the observations was transmitted or digitized (i.e. observational form). BUOY — FM 18-X SHIP — FM 13-X TESAC — FM 64-IX WAVEOB — FM 65-IX BUFR — FM 94-XI Other WMO codes added as needed NOTE: Use actual WMO code designator as the abbreviation (e.g. FM 18-X) |
| 29 | wdpth |  | Water depth (nearest whole metre) |
| 30 | plt |  | Payload type (e.g. DACT, VEEP, GSBP, ZENO, ODAS33, etc.) Details should be provided regarding each type of payload (payload description) |
| 31 | DI | AV NA | Digital image — a photograph or schematic of the platform and equipment Available in digital file Not available |
| 32 | WebA |  | Web address (URL) where additional information can be obtained |

ANEMOMETER (AN)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | anmI |  | Anemometer instrument type |
|  |  | P | Propeller/vane |
|  |  | TC | Three cup |
|  |  | FC | Four cup |
|  |  | S | Sonic |
|  |  | WT | WOTAN (wind observation through ambient noise) |
|  |  | UN | Unknown |
|  |  | OT | Other (define in footnote) |
| 4 | aMS |  | Anemometer — model (manufacturer/series no.) |
| 5 | anmL |  | Anemometer — location |
|  |  | FM | Foremast |
|  |  | AM | Aftmast |
|  |  | CM | Centremast (mainmast) |
|  |  | RY | Right yardarm |
|  |  | LY | Left yardarm |
|  |  | UN | Unknown |
|  |  | OT | Other (define in footnote) |
| 6 | anDB |  | Anemometer — distance from the bow or front of platform (metres to tenths) |
| 7 | anDC |  | Anemometer — distance from centre line or from centre of discus (metres to tenths) |
| 8 | hwl |  | Anemometer — height above water line (metres to tenths). Value can be negative for WOTAN |
| 9 | ouAN |  | Anemometer — operational range and units of measurement (e.g. 0 to 60 m s–1;000 to 360度) |
| 10 | sfWD |  | Sampling frequency (Hz) — wind direction (e.g. 1.28 Hz) |
| 11 | sfWS |  | Sampling frequency (Hz) — wind speed (e.g. 1.28 Hz) |
| 12 | apWD |  | Averaging period (minutes to tenths) — wind direction (e.g. 8.0 minutes) |
| 13 | apWS |  | Averaging period (minutes to tenths) — wind speed (e.g. 8.0 minutes) |
| 14 | amWS | S V | Averaging method — wind speed Scalar Vector |
| 15 | cmpT |  | Compass type/model no. — anemometer |
| 16 | apWG |  | Averaging period (seconds) — wind gust (e.g. 5 seconds) |
| 17 | amWG | S V | Averaging method — wind gust Scalar Vector |
| 18 | amScd |  | Calibration date — anemometer sensor no. Date sensor was last calibrated (e.g. 2000-7-23) |
| 19 | amID |  | Anemometer sensor installation date (e.g. 1995-2-28). If the direction sensor and speed sensor are separate instruments then use footnote # 1 in the anemometer data record to enter the dates for speed sensor and this position for direction sensor |
| 20 | amSD |  | Anemometer out of service dates (“amSD” is beginning date, “amED” is ending date, e.g. amSD =1996-1-23; amED=1996-2-12). If known these dates should be entered anytime either the direction, speed, or both is unavailable due to equipment outage (non-reporting or invalid reports) |
| 21 | (amED) |  |  |

AIR TEMPERATURE (AT)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | ats |  | Air temperature sensor — instrument type |
|  |  | ER | Electrical resistance thermometer |
|  |  | M | Mercury-in-glass thermometer |
|  |  | MS | Screen shelter — mercury thermometer |
|  |  | A | Alcohol-in-glass thermometer |
|  |  | AS | Screen shelter — alcohol thermometer |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 1 in the air temperature data record) |
| 4 | atsMS |  | Air temperature sensor — model (manufacturer/series no.) |
| 5 | atsL |  | Air temperature sensor — location |
|  |  | FM | Foremast |
|  |  | AM | Aftmast |
|  |  | CM | Centremast (mainmast) |
|  |  | RY | Right yardarm |
|  |  | LY | Left yardarm |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 2 in the air temperature data record) |
| 6 | atsDB |  | Air temperature sensor — distance (metres to tenths) from bow or front of platform NOTE: Leave this field blank if platform is a discus |
| 7 | atsC |  | Air temperature sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | atswl |  | Air temperature sensor — height (metres to tenths) above water line |
| 9 | ouAT |  | Air temperature sensor — operational range and units of measurement (e.g. — 40▲C to+ 50▲C) |
| 10 | sfAT |  | Sampling frequency (Hz) — air temperature sensor (e.g. 1.28 Hz) |
| 11 | apAT |  | Averaging period (minutes to tenths) — air temperature sensor (e.g. 8.0 minutes) |
| 12 | atScd |  | Calibration date — air temperature sensor no. Date sensor was last calibrated (e.g. 2000-7-23) |
| 13 | atID |  | Air temperature sensor installation date (e.g. 1995-2-28) |
| 14 | atSD |  | Air temperature sensor out of service dates (“atSD” is beginning date; “atED” is ending date; e.g. atSD=1996-1-23; atED=1996-2-12). If known these dates should be entered anytime the air temperature is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | atED |  |  |

WATER TEMPERATURE (WT)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | wts |  | Water temperature sensor — instrument type |
|  |  | HC | Hull contact sensor |
|  |  | HT | "Through hull" sensor |
|  |  | RT | Radiation thermometer |
|  |  | ER | Electrical resistance thermometer |
|  |  | TT | Trailing thermistor |
|  |  | BU | Bucket thermometer |
|  |  | CTD | CTD (conductivity-temperature-depth) |
|  |  | STD | STD (salinity-temperature-depth) |
|  |  | RM | Refractometer |
|  |  | XC | XCTD (expendable CTD probe) |
|  |  | NS | Nansen cast |
|  |  | AL | ALACE (autonomus Lagrangian circulation explorer) |
|  |  | XBT | Expendable bathythermograph |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 1 in the water temperature data record) |
| 4 | wtsMS |  | Water (sea) temperature sensor — model (manufacturer/series no.) |
| 5 | wtsL |  | Water temperature sensor — location (e.g. port bow, bottom of discus, etc.) |
| 6 | wtsDB |  | Water temperature sensor — distance (metres to tenths) from the bow or front of platform NOTE: Left blank for discus hulls and subsurface temperatures |
| 7 | wtsC |  | Water temperature sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | dws |  | Depth of water temperature sensor; tenths of metres (e.g. 10.3 m) below the water line |
| 9 | ouWT |  | Operational range and units of measurement — water temperature sensor (e.g. range —4▲C to + 40▲C) |
| 10 | sfWT |  | Sample frequency (Hz) — water temperature sensor (e.g. 1.28 Hz) |
| 11 | apWT |  | Averaging period (minutes to tenths) — water temperature sensor (e.g. 8.0 minutes) |
| 12 | wtScd |  | Calibration date — water temperature sensor no. Date sensor was last calibrated (e.g. 2000-7-23) |
| 13 | wtID |  | Water temperature sensor installation date (e.g. 1995-2-28) |
| 14 | wtSD |  | Water temperature sensor out of service dates (“wtSD” is beginning date; “wtED” is ending date, e.g. wtSD=1996-1-23; wtED=1996-2-12). If known these dates should be entered anytime the water temperature is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | wtED |  |  |

SALINITY (SA)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | Sstp |  | Salinity – sensor type |
|  |  | CTD | CTD (conductivity-temperature-depth) |
|  |  | STD | STD (salinity-temperature-depth) |
|  |  | RM | Refractometer |
|  |  | XC | XCTD (expendable CTD probe) |
|  |  | NS | Nansen cast |
|  |  | AL | ALACE (autonomous Lagrangian circulation explorer) |
|  |  | UN | Unknown |
|  |  | OT | Other (specify in footnote # 1 in the salinity data record) |
| 4 | Ssm |  | Salinity sensor (model/manufacturer/series no.) |
| 5 | SsL |  | Salinity sensor no. — location [NOTE: To be used only for those sensors attached to a platform] |
| 6 | SsDB |  | Salinity sensor no. — distance from bow or front of platform NOTE: To be used only when sensor is attached to a platform (same as location above) |
| 7 | SsC |  | Salinity sensor no. — distance from centre line or centre of discus |
| 8 | dss |  | Depth of salinity sensor no. — metres to tenths (e.g. 10.7 m) of salinity sensor below the water line (surface of the water) |
| 9 | ouSs |  | Salinity sensor — operational range and units of measurement (e.g. 25 to 45 parts per thousand. Salinity is calculated based on the measurement of chlorinity) |
| 10 | sfSs |  | Sample frequency — available only for automated digital sensors |
| 11 | apSs |  | Averaging period — available only for automated digital sensors |
| 12 | mSs |  | Method used to compute the salinity (e.g. chlorinity, electrical conductivity, refractive index, etc.) |
| 13 | SsScd |  | Calibration date — salinity sensor no. Date the sensor was last calibrated (e.g. 2000-2-17) |
| 14 | SsID |  | Salinity sensor installation date (e.g. 1995-2-28) |
| 15 | SsSD |  | Salinity sensor out of service dates (“SsSD” is beginning date; “SsED” is ending date, e.g. SsSD =1996-1-23; SsED=1996-2-12). If known these dates should be entered anytime the salinity is unavailable due to equipment outage (non-reporting or invalid reports) |
| 16 | SsED |  |  |

BAROMETRIC PRESSURE (BP)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | bps |  | Barometric pressure sensor — instrument type |
| 4 | bpsMS |  | Barometric pressure sensor — model (manufacturer/series no.) |
| 5 | bpsL |  | Barometric pressure sensor — location (e.g. centremast) |
| 6 | bpsDB |  | Barometric pressure sensor — distance (metres to tenths) from the bow or front of platform NOTE: Leave this field blank if platform is a discus |
| 7 | bpsC |  | Barometric pressure sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | bpswl |  | Barometric pressure sensor — height (metres to tenths) above water line |
| 9 | ouBP |  | Barometric pressure sensor — operational range and units of measurement (e.g. 900–1 100 hPa) |
| 10 | sfBP |  | Sampling frequency (Hz) — barometric pressure sensor (e.g. 1.28 Hz) |
| 11 | apBP |  | Averaging period (minutes to tenths) — barometric pressure sensor (e.g. 8.0 minutes) |
| 12 | bpScd |  | Calibration date — barometric pressure sensor no. Latest date of calibration (e.g. 2000-2-17) |
| 13 | bpsID |  | Barometric pressure sensor installation date (e.g. 1995-2-28) |
| 14 | bpsSD |  | Barometric pressure sensor out of service dates (“bpsSD” is beginning date; “bpsED” is ending date, e.g. bpsSD =1996-1-23; bpsED=1996-2-12). If known these dates should be entered anytime the barometric pressure is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | bpsED |  |  |

RELATIVE HUMIDITY (RH)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | hs |  | Relative humidity (wet bulb/dew point) sensor — instrument type |
| 4 | hsMS |  | Relative humidity (wet bulb/dew point) sensor — model (manufacturer/series no.) |
| 5 | hsL |  | Relative humidity (wet bulb/dew point) sensor — location (left yardarm mast) |
| 6 | hsDB |  | Relative humidity sensor — distance (metres to tenths) from the bow or front of platform NOTE: Leave this field blank if platform is a discus |
| 7 | hsC |  | Relative humidity sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | hswl |  | Relative humidity sensor — height (metres to tenths) above water line |
| 9 | ouhs |  | Relative humidity (wet bulb/dew point) sensor — operational range and units of measurement (e.g. range 0–100 per cent) |
| 10 | sfhs |  | Sampling frequency (Hz) — relative humidity (wet bulb/dew point) sensor (e.g. 1 Hz) |
| 11 | aphs |  | Averaging period (minutes) — relative humidity (wet bulb/dew point) sensor (e.g.1 min.) |
| 12 | hsScd |  | Calibration date — relative humidity (wet bulb/dew point) sensor no. Latest date the sensor was calibrated (e.g. 2000-2-17) |
| 13 | hsID |  | Relative humidity (wet bulb/dew point) sensor installation date (e.g. 1995-2-28) |
| 14 | hsSD |  | Relative humidity (wet bulb/dew point) sensor out of service dates (“hsSD” is beginning date; “hsED” is ending date, e.g. hsSD =1996-1-23; hsED=1996-2-12). If known, these dates should be entered anytime the relative humidity (wet bulb/dew point) is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | hsED |  |  |

PRECIPITATION (PG)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | pg |  | Precipitation gauge — instrument type (e. g. weighing bucket, tipping bucket, etc.) |
| 4 | pgMS |  | Precipitation gauge — model (manufacturer/series no.) |
| 5 | pgL |  | Precipitation gauge — location |
| 6 | pgDB |  | Precipitation gauge — distance (metres to tenths) from the bow or front of platform |
| 7 | pgC |  | Precipitation gauge — distance (metres to tenths) from centre line or off centre of a discus |
| 8 | pgwl |  | Precipitation gauge — height (metres to tenths) above water line |
| 9 | oupg |  | Precipitation gauge — operational range and units of measurement (e.g. 0 to 25 cm per hour) |
| 10 | sfPG |  | Sampling frequency — precipitation gauge (e.g. continuous) |
| 11 | apPG |  | Averaging period — precipitation gauge (e.g. 6 hours; then reset) |
| 12 | pgScd |  | Calibration date — precipitation gauge no. Latest date sensor/gauge was calibrated (e.g. 2000-2-17) |
| 13 | pgID |  | Precipitation gauge installation date (e.g. 1995-2-28) |
| 14 | pgSD |  | Precipitation gauge out of service dates (“pgSD” is beginning date; “pgED” is ending date, e.g. pgSD=1996-1-23, pgED=1996=2=12). If known, these dates should be entered anytime the precipitation measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | pgED |  |  |

RADIATION (RD)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | srs |  | Solar radiation sensor — instrument type |
| 4 | rMS |  | Radiation sensor — model (manufacturer/series no.) |
| 5 | rsL |  | Radiation sensor — location (e.g. foremast) |
| 6 | rsDB |  | Radiation sensor — distance (metres to tenths) from the bow or front of platform NOTE: Leave this field blank if platform is a discus |
| 7 | rsC |  | Radiation sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | srwl |  | Solar radiation sensor — height (metres to tenths) above water line |
| 9 | ours |  | Radiation sensor — operational range and units of measurement (e.g. 0.07–1.65 cal cm–2 min–1) |
| 10 | sfSR |  | Sampling frequency (Hz) — solar radiation sensor (e.g. 1 Hz) |
|  | apSR |  | Averaging period (minutes to tenths) — solar radiation sensor (e.g. 8.0 minutes) |
|  | srScd |  | Calibration date — solar radiation sensor no. Latest date the sensor was calibrated (e.g. 2000-2-17) |
| 11 | rsID |  | Radiation sensor installation date (e.g. 1995-2-28) |
| 12 | rsSD |  | Radiation sensor out of service dates (“rsSD” is beginning date: “rsED” is ending date, e.g. rsSD=1996-1-23; rsED=1996-2-12). If known, these dates should be entered anytime the radiation measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| 13 | rsED |  |  |

OCEAN CURRENTS (CR)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | OC | C M E | Ocean current speed reported Calculated Measured Estimated |
| 4 | TSmoc |  | Type sensor measuring ocean currents (type/model/manufacturer) |
| 5 | dmOC |  | Depth of measurement (in metres, e.g. 10 m) of the ocean current |
| 6 | ouOC |  | Ocean currents — operational range and units of measurement (range, e.g. — 10 m s–1 to +10 m s–1) |
| 7 | sfOC |  | Sampling frequency (Hz) — ocean currents (e.g. 0.667 Hz) |
| 8 | apOC |  | Averaging period (minutes to tenths) — ocean currents (e.g. 20.0 minutes) |
| 9 | ocScd |  | Calibration date — ocean current sensor (e.g. 2000-2-17) |
| 10 | ocID |  | Ocean current sensor installation date (e.g. 1995-2-28) |
| 11 | ocSD |  | Ocean current sensor out of service dates (“ocSD” is beginning date; “ocED” is ending date, e.g. ocSD=1996-1-23; ocED=1996-2-12). If known, these dates should be entered anytime the ocean current measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| 12 | ocED |  |  |

WAVE SPECTRA (WS)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | wasp |  | Wave spectra — type of surface elevation sensor (from which wave spectra is derived) |
| 4 | Digf |  | Digital filter used — wave spectra |
| 5 | Nblks |  | Number of blocks used for averaging — wave spectra 4 Npts Number of points in each block |
| 6 | Npts |  | Number of points in each block — wave spectra |
| 7 | spAT |  | Spectral analysis technique (e.g. FFT, MEM, etc.) |
| 8 | sfWAS |  | Sampling frequency — wave spectra (e.g. 2.56 Hz) |
| 9 | apWAS |  | Averaging period — length of record for averaging period — wave spectra (e.g. 20 minutes) |

HORIZONTAL VISIBILITY (HV)

| sequence number | Field abbreviation | Input codes | Description of fields |
| --- | --- | --- | --- |
| 1 | Sno |  | Sensor ID |
| 2 | ID |  | ODAS ID of the Platform that sensor was on board, connective with HR. |
| 3 | hvm | MAN ATM | Horizontal visibility Manual Automated |
| 4 | hvit |  | Instrument type (automated sensor) — model/manufacturer/series no. |
| 5 | hvl |  | Location — horizontal visibility sensor no. |
| 6 | hvDB |  | Horizontal visibility sensor — distance (metres to tenths) from the bow or front of platform NOTE: Leave this field blank if platform is a discus |
| 7 | hvC |  | Horizontal visibility sensor — distance (metres to tenths) from centre line or centre of discus |
| 8 | hvwl |  | Horizontal visibility sensor — height (metres to tenths) above water line |
| 9 | hvou |  | Horizontal visibility sensor — operational range and units of measurement (e.g. 0000 to 9 999 m or < 0.1 km –10 km) |
| 10 | hvsf |  | Sampling frequency — horizontal visibility sensor no. |
| 11 | hvap |  | Averaging period — horizontal visibility sensor no. |
| 12 | hvScd |  | Calibration date — horizontal visibility sensor no. Latest date sensor was calibrated (e.g. 2000-2-17) |
| 13 | hvID |  | Horizontal visibility sensor installation date (e.g. 1995-2-28) |
| 14 | hvSD |  | Horizontal visibility sensor out of service dates (“hvSD” is beginning date; “hvED” ending date, e.g. hvSD=1996-1-23; hvED=1996-2-12). If known, these dates should be entered anytime the visibility measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| 15 | hvED |  |  |

Annex 2: XML Schema for ODAS metadata

1. XML Schema for Header record

<?xml version="1.0" encoding="utf-8" ?>

<xs:schema id="ODASMetadata_1.1" elementFormDefault="qualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:element name="ODASDataSet">

<xs:complexType>

<xs:sequence>

<xs:element name="HR">

<xs:complexType>

<xs:sequence>

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="mc">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ts" type="tsCd"></xs:element>

<xs:element name="WMOn">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="stn" type="xs:string" />

<xs:element name="AIn" type="xs:int" />

<xs:element name="ind" type="xs:dateTime" />

<xs:element name="oed" type="xs:dateTime" />

<xs:element name="ltd" type="xs:dateTime" />

<xs:element name="cnty" type="cntyCd" />

<xs:element name="ragy" type="xs:string" />

<xs:element name="ldmu" type="xs:dateTime" />

<xs:element name="DA" type="DACd" />

<xs:element name="Lat" type="xs:float" />

<xs:element name="Lon" type="xs:float" />

<xs:element name="ltlat" type="xs:float" />

<xs:element name="ltlon" type="xs:float" />

<xs:element name="atv" type="xs:boolean" />

<xs:element name="WC" type="xs:float" />

<xs:element name="lngth" type="xs:float" />

<xs:element name="Brth" type="xs:float" />

<xs:element name="Diam" type="xs:float" />

<xs:element name="Hult" type="HultCd" />

<xs:element name="Huln" type="xs:string" />

<xs:element name="Mtyp" type="MtypCd" />

<xs:element name="Cmsy" type="CmsyCd" />

<xs:element name="Stt" type="xs:string" />

<xs:element name="Foo" type="xs:string" />

<xs:element name="dfmt" type="xs:string" />

<xs:element name="wdpth" type="xs:int" />

<xs:element name="plt" type="xs:string" />

<xs:element name="DI" type="DICd" />

<xs:element name="WebA" type="xs:string" />

<xs:element name="Footnote1" type="xs:string" />

<xs:element name="Footnote2" type="xs:string" />

<xs:element name="Footnote3" type="xs:string" />

<xs:element name="Footnote4" type="xs:string" />

<xs:element name="Footnote5" type="xs:string" />

</xs:sequence>

</xs:complexType>

</xs:element>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:simpleType name="tsCd">

<xs:restriction base="xs:string">

<xs:enumeration value="DB" />

<xs:enumeration value="ID" />

<xs:enumeration value="DP" />

<xs:enumeration value="IS" />

<xs:enumeration value="AL" />

<xs:enumeration value="CM" />

<xs:enumeration value="PF" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="cntyCd">

<xs:restriction base="xs:string">

<xs:enumeration value="AFGHANISTAN" />

<xs:enumeration value="ALBANIA" />

<xs:enumeration value="ALGERIA" />

<xs:enumeration value="AMERICAN SAMOA" />

<xs:enumeration value="ANDORRA" />

<xs:enumeration value="ANGOLA" />

<xs:enumeration value="ANGUILLA" />

<xs:enumeration value="ANTARCTICA" />

<xs:enumeration value="ANTIGUA AND BARBUDA" />

<xs:enumeration value="ARGENTINA" />

<xs:enumeration value="ARMENIA" />

<xs:enumeration value="ARUBA" />

<xs:enumeration value="AUSTRALIA" />

<xs:enumeration value="AUSTRIA" />

<xs:enumeration value="AZERBAIJAN" />

<xs:enumeration value="BAHAMAS" />

<xs:enumeration value="BAHRAIN" />

<xs:enumeration value="BANGLADESH" />

<xs:enumeration value="BARBADOS" />

<xs:enumeration value="BELARUS" />

<xs:enumeration value="BELGIUM" />

<xs:enumeration value="BELIZE" />

<xs:enumeration value="BENIN" />

<xs:enumeration value="BERMUDA" />

<xs:enumeration value="BHUTAN" />

<xs:enumeration value="BOLIVIA" />

<xs:enumeration value="BOSNIA AND HERZEGOWINA" />

<xs:enumeration value="BOTSWANA" />

<xs:enumeration value="BOUVET ISLAND" />

<xs:enumeration value="BRAZIL" />

<xs:enumeration value="BRAZIL/FRANCE/USA" />

<xs:enumeration value="BRITISH INDIAN OCEAN TERRITORY" />

<xs:enumeration value="BRUNEI DARUSSALAM" />

<xs:enumeration value="BULGARIA" />

<xs:enumeration value="BURKINA FASO" />

<xs:enumeration value="BURUNDI" />

<xs:enumeration value="CAMBODIA" />

<xs:enumeration value="CAMEROON" />

<xs:enumeration value="CANADA" />

<xs:enumeration value="CAPE VERDE" />

<xs:enumeration value="CAYMAN ISLANDS" />

<xs:enumeration value="CENTRAL AFRICAN REPUBLIC" />

<xs:enumeration value="CHAD" />

<xs:enumeration value="CHILE" />

<xs:enumeration value="CHINA" />

<xs:enumeration value="CHRISTMAS ISLAND" />

<xs:enumeration value="COCOS (KEELING) ISLANDS" />

<xs:enumeration value="COLOMBIA" />

<xs:enumeration value="COMOROS" />

<xs:enumeration value="CONGO" />

<xs:enumeration value="COOK ISLANDS" />

<xs:enumeration value="COSTA RICA" />

<xs:enumeration value="COTE D'IVOIRE" />

<xs:enumeration value="CROATIA (local name: Hrvatska)" />

<xs:enumeration value="CUBA" />

<xs:enumeration value="CYPRUS" />

<xs:enumeration value="CZECH REPUBLIC" />

<xs:enumeration value="DENMARK" />

<xs:enumeration value="DJIBOUTI" />

<xs:enumeration value="DOMINICA" />

<xs:enumeration value="DOMINICAN REPUBLIC" />

<xs:enumeration value="EAST TIMOR" />

<xs:enumeration value="ECUADOR" />

<xs:enumeration value="EGYPT" />

<xs:enumeration value="EL SALVADOR" />

<xs:enumeration value="EQUATORIAL GUINEA" />

<xs:enumeration value="ERITREA" />

<xs:enumeration value="ESTONIA" />

<xs:enumeration value="ETHIOPIA" />

<xs:enumeration value="EUROPEAN UNION" />

<xs:enumeration value="FALKLAND ISLANDS (MALVINAS)" />

<xs:enumeration value="FAROE ISLANDS" />

<xs:enumeration value="FIJI" />

<xs:enumeration value="FINLAND" />

<xs:enumeration value="FRANCE" />

<xs:enumeration value="FRANCE, METROPOLITAN" />

<xs:enumeration value="FRENCH GUIANA" />

<xs:enumeration value="FRENCH POLYNESIA" />

<xs:enumeration value="FRENCH SOUTHERN TERRITORIES" />

<xs:enumeration value="GABON" />

<xs:enumeration value="GAMBIA" />

<xs:enumeration value="GEORGIA" />

<xs:enumeration value="GERMANY" />

<xs:enumeration value="GHANA" />

<xs:enumeration value="GIBRALTAR" />

<xs:enumeration value="GREECE" />

<xs:enumeration value="GREENLAND" />

<xs:enumeration value="GRENADA" />

<xs:enumeration value="GUADELOUPE" />

<xs:enumeration value="GUAM" />

<xs:enumeration value="GUATEMALA" />

<xs:enumeration value="GUINEA" />

<xs:enumeration value="GUINEA-BISSAU" />

<xs:enumeration value="GUYANA" />

<xs:enumeration value="HAITI" />

<xs:enumeration value="HEARD AND MC DONALD ISLANDS" />

<xs:enumeration value="HONDURAS" />

<xs:enumeration value="HONG KONG, CHINA" />

<xs:enumeration value="HUNGARY" />

<xs:enumeration value="ICELAND" />

<xs:enumeration value="INDIA" />

<xs:enumeration value="INDONESIA" />

<xs:enumeration value="IRAN (ISLAMIC REPUBLIC OF)" />

<xs:enumeration value="IRAQ" />

<xs:enumeration value="IRELAND" />

<xs:enumeration value="ISRAEL" />

<xs:enumeration value="ITALY" />

<xs:enumeration value="JAMAICA" />

<xs:enumeration value="JAPAN" />

<xs:enumeration value="JAPAN/USA" />

<xs:enumeration value="JORDAN" />

<xs:enumeration value="KAZAKHSTAN" />

<xs:enumeration value="KENYA" />

<xs:enumeration value="KIRIBATI" />

<xs:enumeration value="KOREA (REPUBLIC OF)" />

<xs:enumeration value="KOREA, DEMOCRATIC PEOPLE'S REPUBLIC OF" />

<xs:enumeration value="KUWAIT" />

<xs:enumeration value="KYRGYZSTAN" />

<xs:enumeration value="LAO PEOPLE'S DEMOCRATIC REPUBLIC" />

<xs:enumeration value="LATVIA" />

<xs:enumeration value="LEBANON" />

<xs:enumeration value="LESOTHO" />

<xs:enumeration value="LIBERIA" />

<xs:enumeration value="LIBYAN ARAB JAMAHIRIYA" />

<xs:enumeration value="LIECHTENSTEIN" />

<xs:enumeration value="LITHUANIA" />

<xs:enumeration value="LUXEMBOURG" />

<xs:enumeration value="MACAU" />

<xs:enumeration value="MACEDONIA, THE FORMER YUGOSLAV REPUBLIC OF" />

<xs:enumeration value="MADAGASCAR" />

<xs:enumeration value="MALAWI" />

<xs:enumeration value="MALAYSIA" />

<xs:enumeration value="MALDIVES" />

<xs:enumeration value="MALI" />

<xs:enumeration value="MALTA" />

<xs:enumeration value="MARSHALL ISLANDS" />

<xs:enumeration value="MARTINIQUE" />

<xs:enumeration value="MAURITANIA" />

<xs:enumeration value="MAURITIUS" />

<xs:enumeration value="MAYOTTE" />

<xs:enumeration value="MEXICO" />

<xs:enumeration value="MICRONESIA, FEDERATED STATES OF" />

<xs:enumeration value="MOLDOVA, REPUBLIC OF" />

<xs:enumeration value="MONACO" />

<xs:enumeration value="MONGOLIA" />

<xs:enumeration value="MONTSERRAT" />

<xs:enumeration value="MOROCCO" />

<xs:enumeration value="MOZAMBIQUE" />

<xs:enumeration value="MYANMAR" />

<xs:enumeration value="NAMIBIA" />

<xs:enumeration value="NAURU" />

<xs:enumeration value="NEPAL" />

<xs:enumeration value="NETHERLANDS" />

<xs:enumeration value="NETHERLANDS ANTILLES" />

<xs:enumeration value="NEW CALEDONIA" />

<xs:enumeration value="NEW ZEALAND" />

<xs:enumeration value="NICARAGUA" />

<xs:enumeration value="NIGER" />

<xs:enumeration value="NIGERIA" />

<xs:enumeration value="NIUE" />

<xs:enumeration value="NORFOLK ISLAND" />

<xs:enumeration value="NORTHERN MARIANA ISLANDS" />

<xs:enumeration value="NORWAY" />

<xs:enumeration value="OMAN" />

<xs:enumeration value="Pacific Islands Countries and Territorries" />

<xs:enumeration value="PAKISTAN" />

<xs:enumeration value="PALAU" />

<xs:enumeration value="PANAMA" />

<xs:enumeration value="PAPUA NEW GUINEA" />

<xs:enumeration value="PARAGUAY" />

<xs:enumeration value="PERU" />

<xs:enumeration value="PHILIPPINES" />

<xs:enumeration value="PITCAIRN" />

<xs:enumeration value="POLAND" />

<xs:enumeration value="PORTUGAL" />

<xs:enumeration value="PUERTO RICO" />

<xs:enumeration value="QATAR" />

<xs:enumeration value="REUNION" />

<xs:enumeration value="ROMANIA" />

<xs:enumeration value="RUSSIAN FEDERATION" />

<xs:enumeration value="RWANDA" />

<xs:enumeration value="SAINT KITTS AND NEVIS" />

<xs:enumeration value="SAINT LUCIA" />

<xs:enumeration value="SAINT VINCENT AND THE GRENADINES" />

<xs:enumeration value="SAMOA" />

<xs:enumeration value="SAN MARINO" />

<xs:enumeration value="SAO TOME AND PRINCIPE" />

<xs:enumeration value="SAUDI ARABIA" />

<xs:enumeration value="SENEGAL" />

<xs:enumeration value="SEYCHELLES" />

<xs:enumeration value="SIERRA LEONE" />

<xs:enumeration value="SINGAPORE" />

<xs:enumeration value="SLOVAKIA (Slovak Republic)" />

<xs:enumeration value="SLOVENIA" />

<xs:enumeration value="SOLOMON ISLANDS" />

<xs:enumeration value="SOMALIA" />

<xs:enumeration value="SOUTH AFRICA" />

<xs:enumeration value="SOUTH GEORGIA AND THE SOUTH SANDWICH ISLANDS" />

<xs:enumeration value="SPAIN" />

<xs:enumeration value="SRI LANKA" />

<xs:enumeration value="ST. HELENA" />

<xs:enumeration value="ST. PIERRE AND MIQUELON" />

<xs:enumeration value="SUDAN" />

<xs:enumeration value="SURINAME" />

<xs:enumeration value="SVALBARD AND JAN MAYEN ISLANDS" />

<xs:enumeration value="SWAZILAND" />

<xs:enumeration value="SWEDEN" />

<xs:enumeration value="SWITZERLAND" />

<xs:enumeration value="SYRIAN ARAB REPUBLIC" />

<xs:enumeration value="TAIWAN, PROVINCE OF CHINA" />

<xs:enumeration value="TAJIKISTAN" />

<xs:enumeration value="TANZANIA, UNITED REPUBLIC OF" />

<xs:enumeration value="THAILAND" />

<xs:enumeration value="TOGO" />

<xs:enumeration value="TOKELAU" />

<xs:enumeration value="TONGA" />

<xs:enumeration value="TRINIDAD AND TOBAGO" />

<xs:enumeration value="TUNISIA" />

<xs:enumeration value="TURKEY" />

<xs:enumeration value="TURKMENISTAN" />

<xs:enumeration value="TURKS AND CAICOS ISLANDS" />

<xs:enumeration value="TUVALU" />

<xs:enumeration value="UGANDA" />

<xs:enumeration value="UKRAINE" />

<xs:enumeration value="UNITED ARAB EMIRATES" />

<xs:enumeration value="UNITED KINGDOM" />

<xs:enumeration value="UNITED NATIONS" />

<xs:enumeration value="UNITED STATES" />

<xs:enumeration value="UNITED STATES MINOR OUTLYING ISLANDS" />

<xs:enumeration value="UNKNOWN" />

<xs:enumeration value="URUGUAY" />

<xs:enumeration value="UZBEKISTAN" />

<xs:enumeration value="VANUATU" />

<xs:enumeration value="VATICAN CITY STATE (HOLY SEE)" />

<xs:enumeration value="VENEZUELA" />

<xs:enumeration value="VIET NAM" />

<xs:enumeration value="VIRGIN ISLANDS (BRITISH)" />

<xs:enumeration value="VIRGIN ISLANDS (U.S.)" />

<xs:enumeration value="WALLIS AND FUTUNA ISLANDS" />

<xs:enumeration value="WESTERN SAHARA" />

<xs:enumeration value="YEMEN" />

<xs:enumeration value="YUGOSLAVIA" />

<xs:enumeration value="ZAIRE" />

<xs:enumeration value="ZAMBIA" />

<xs:enumeration value="ZIMBABWE" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="DACd">

<xs:restriction base="xs:string">

<xs:enumeration value="1" />

<xs:enumeration value="2" />

<xs:enumeration value="3" />

<xs:enumeration value="4" />

<xs:enumeration value="5" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="HultCd">

<xs:restriction base="xs:string">

<xs:enumeration value="DS" />

<xs:enumeration value="BS" />

<xs:enumeration value="RS" />

<xs:enumeration value="SP" />

<xs:enumeration value="OD" />

<xs:enumeration value="MM" />

<xs:enumeration value="TR" />

<xs:enumeration value="CN" />

<xs:enumeration value="OR" />

<xs:enumeration value="DR" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="MtypCd">

<xs:restriction base="xs:string">

<xs:enumeration value="AC" />

<xs:enumeration value="ST" />

<xs:enumeration value="FC" />

<xs:enumeration value="PC" />

<xs:enumeration value="DT" />

<xs:enumeration value="HS" />

<xs:enumeration value="TS" />

<xs:enumeration value="WS" />

<xs:enumeration value="PA" />

<xs:enumeration value="NL" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="CmsyCd">

<xs:restriction base="xs:string">

<xs:enumeration value="GO" />

<xs:enumeration value="AR" />

<xs:enumeration value="GA" />

<xs:enumeration value="RF" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="DICd">

<xs:restriction base="xs:string">

<xs:enumeration value="AV" />

<xs:enumeration value="NA" />

</xs:restriction>

</xs:simpleType>

</xs:schema>

2. XML Schema for Sensor records

<?xml version="1.0" encoding="utf-8" ?>

<xs:schema id="ODASSensor_1.1" elementFormDefault="qualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:element name="SensorSet">

<xs:complexType>

<xs:sequence>

<xs:element name="ANSet" type="ANSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="ATSet" type="ATSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="WTSet" type="WTSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="SASet" type="SASet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="BPSet" type="BPSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="RHSet" type="RHSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="PGSet" type="PGSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="RDSet" type="RDSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="CRSet" type="CRSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="WSSet" type="WSSet_Type" minOccurs="0" maxOccurs="unbounded" />

<xs:element name="HVSet" type="HVSet_Type" minOccurs="0" maxOccurs="unbounded" />

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:complexType name="ANSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="anmI">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="P" />

<xs:enumeration value="TC" />

<xs:enumeration value="FC" />

<xs:enumeration value="S" />

<xs:enumeration value="WT" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="aMS" type="xs:string"></xs:element>

<xs:element name="anmL">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="FM" />

<xs:enumeration value="AM" />

<xs:enumeration value="CM" />

<xs:enumeration value="RY" />

<xs:enumeration value="LY" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="anDB" type="xs:float" />

<xs:element name="anDC" type="xs:float" />

<xs:element name="hwl" type="xs:float" />

<xs:element name="minWS" type="xs:float" />

<xs:element name="maxWS" type="xs:float" />

<xs:element name="unitWS" type="xs:float" />

<xs:element name="minWD" type="xs:float" />

<xs:element name="maxWD" type="xs:float" />

<xs:element name="unitWD" type="xs:float" />

<xs:element name="sfWD" type="xs:float" />

<xs:element name="sfWS" type="xs:float" />

<xs:element name="apWD" type="xs:float" />

<xs:element name="apWS" type="xs:float" />

<xs:element name="amWS">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="S" />

<xs:enumeration value="V" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="cmpT" type="xs:string" />

<xs:element name="apWG" type="xs:string" />

<xs:element name="amWG">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="S" />

<xs:enumeration value="V" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="amScd" type="xs:string" />

<xs:element name="amID" type="xs:string" />

<xs:element name="amSD" type="xs:string" />

<xs:element name="amED" type="xs:string" />

<xs:element name="footnote1" type="xs:string" />

<xs:element name="footnote2" type="xs:string" />

<xs:element name="footnote3" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="ATSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ats">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="ER" />

<xs:enumeration value="M" />

<xs:enumeration value="MS" />

<xs:enumeration value="A" />

<xs:enumeration value="AS" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="atsMS" type="xs:string"></xs:element>

<xs:element name="atsL">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="FM" />

<xs:enumeration value="AM" />

<xs:enumeration value="CM" />

<xs:enumeration value="RY" />

<xs:enumeration value="LY" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="atsDB" type="xs:float" />

<xs:element name="atsC" type="xs:float" />

<xs:element name="atswl" type="xs:float" />

<xs:element name="MinAT" type="xs:float" />

<xs:element name="MaxAT" type="xs:float" />

<xs:element name="uAT" type="xs:float" />

<xs:element name="sfAT" type="xs:float" />

<xs:element name="apAT" type="xs:float" />

<xs:element name="atScd" type="xs:dateTime" />

<xs:element name="atID" type="xs:dateTime" />

<xs:element name="atSD" type="xs:dateTime" />

<xs:element name="atED" type="xs:dateTime" />

<xs:element name="footnote1" type="xs:string" />

<xs:element name="footnote2" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="WTSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="wts">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="HC" />

<xs:enumeration value="HT" />

<xs:enumeration value="RT" />

<xs:enumeration value="ER" />

<xs:enumeration value="TT" />

<xs:enumeration value="BU" />

<xs:enumeration value="CTD" />

<xs:enumeration value="STD" />

<xs:enumeration value="RM" />

<xs:enumeration value="XC" />

<xs:enumeration value="NS" />

<xs:enumeration value="AL" />

<xs:enumeration value="XBT" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="wtsMS" type="xs:string"></xs:element>

<xs:element name="wtsL" type="xs:string" />

<xs:element name="wtsDB" type="xs:float" />

<xs:element name="wtsC" type="xs:float" />

<xs:element name="dws" type="xs:float" />

<xs:element name="MinWT" type="xs:float" />

<xs:element name="MaxWT" type="xs:float" />

<xs:element name="UWT" type="xs:float" />

<xs:element name="sfWT" type="xs:float" />

<xs:element name="apWT" type="xs:float" />

<xs:element name="wtScd" type="xs:dateTime" />

<xs:element name="wtID" type="xs:dateTime" />

<xs:element name="wtSD" type="xs:dateTime" />

<xs:element name="wtED" type="xs:dateTime" />

<xs:element name="footnote1" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="SASet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="Sstp">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="CTD" />

<xs:enumeration value="STD" />

<xs:enumeration value="RM" />

<xs:enumeration value="XC" />

<xs:enumeration value="NS" />

<xs:enumeration value="AL" />

<xs:enumeration value="UN" />

<xs:enumeration value="OT" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ssm" type="xs:string" />

<xs:element name="ssL" type="xs:string" />

<xs:element name="ssDB" type="xs:float" />

<xs:element name="ssC" type="xs:float" />

<xs:element name="dss" type="xs:float" />

<xs:element name="MinSs" type="xs:float" />

<xs:element name="MaxSs" type="xs:float" />

<xs:element name="USs" type="xs:float" />

<xs:element name="sfSs" type="xs:float" />

<xs:element name="apSs" type="xs:float" />

<xs:element name="mSs" type="xs:string" />

<xs:element name="Ssscd" type="xs:dateTime" />

<xs:element name="SsID" type="xs:dateTime" />

<xs:element name="SsSD" type="xs:dateTime" />

<xs:element name="SsED" type="xs:dateTime" />

<xs:element name="footnote1" type="xs:string" />

<xs:element name="footnote2" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="BPSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="Bps" type="xs:string" />

<xs:element name="bpsMS" type="xs:string" />

<xs:element name="bpsL" type="xs:string" />

<xs:element name="bpsDB" type="xs:string" />

<xs:element name="bpsC" type="xs:string" />

<xs:element name="Bpswl" type="xs:string" />

<xs:element name="ouBP" type="xs:string" />

<xs:element name="SfBP" type="xs:string" />

<xs:element name="ApBP" type="xs:string" />

<xs:element name="bpScd" type="xs:string" />

<xs:element name="bpsID" type="xs:string" />

<xs:element name="bpsSD" type="xs:string" />

<xs:element name="bpsED" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="RHSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="hs" type="xs:string" />

<xs:element name="hsMS" type="xs:string" />

<xs:element name="hsL" type="xs:string" />

<xs:element name="hsDB" type="xs:string" />

<xs:element name="hsC" type="xs:string" />

<xs:element name="hswl" type="xs:string" />

<xs:element name="ouHS" type="xs:string" />

<xs:element name="sfhs" type="xs:string" />

<xs:element name="apHS" type="xs:string" />

<xs:element name="hsScd" type="xs:string" />

<xs:element name="hsID" type="xs:string" />

<xs:element name="hsSD" type="xs:string" />

<xs:element name="hsED" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="PGSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="pg" type="xs:string" />

<xs:element name="pgMS" type="xs:string" />

<xs:element name="pgL" type="xs:string" />

<xs:element name="pgDB" type="xs:string" />

<xs:element name="pgC" type="xs:string" />

<xs:element name="pgwl" type="xs:string" />

<xs:element name="ouPG" type="xs:string" />

<xs:element name="sfPG" type="xs:string" />

<xs:element name="apPG" type="xs:string" />

<xs:element name="pgScd" type="xs:string" />

<xs:element name="pgID" type="xs:string" />

<xs:element name="pgSD" type="xs:string" />

<xs:element name="pgED" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="RDSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="srs" type="xs:string" />

<xs:element name="rMS" type="xs:string" />

<xs:element name="rsL" type="xs:string" />

<xs:element name="rsDB" type="xs:string" />

<xs:element name="rsC" type="xs:string" />

<xs:element name="srwl" type="xs:string" />

<xs:element name="ours" type="xs:string" />

<xs:element name="sfSR" type="xs:string" />

<xs:element name="apSR" type="xs:string" />

<xs:element name="srScd" type="xs:string" />

<xs:element name="srScd1" type="xs:string" />

<xs:element name="rsID" type="xs:string" />

<xs:element name="hsSD" type="xs:string" />

<xs:element name="hsED" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="CRSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="OC">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="C" />

<xs:enumeration value="M" />

<xs:enumeration value="E" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="TSmoc" type="xs:string" />

<xs:element name="ocMS" type="xs:string" />

<xs:element name="dmOC" type="xs:string" />

<xs:element name="ouOC" type="xs:string" />

<xs:element name="sfOC" type="xs:string" />

<xs:element name="apOC" type="xs:string" />

<xs:element name="ocScd" type="xs:string" />

<xs:element name="ocID" type="xs:string" />

<xs:element name="ocSD" type="xs:string" />

<xs:element name="ocED" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="WSSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="wasp" type="xs:string" />

<xs:element name="Digf" type="xs:string" />

<xs:element name="Nblks" type="xs:string" />

<xs:element name="Npts" type="xs:string" />

<xs:element name="spAT" type="xs:string" />

<xs:element name="SfWAS" type="xs:string" />

<xs:element name="apWAS" type="xs:string" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="HVSet_Type">

<xs:sequence>

<xs:element name="Sno" type="xs:integer" />

<xs:element name="ID">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="hvm">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:enumeration value="MAN" />

<xs:enumeration value="ATM" />

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="hvit" type="xs:string" />

<xs:element name="hvMS" type="xs:string" />

<xs:element name="hvl" type="xs:string" />

<xs:element name="hvDB" type="xs:string" />

<xs:element name="hvC" type="xs:string" />

<xs:element name="hvwl" type="xs:string" />

<xs:element name="HVou" type="xs:string" />

<xs:element name="hvsf" type="xs:string" />

<xs:element name="hvAP" type="xs:string" />

<xs:element name="hsScd" type="xs:string" />

<xs:element name="hvID" type="xs:string" />

<xs:element name="hvSD" type="xs:string" />

<xs:element name="hvED" type="xs:string" />

</xs:sequence>

</xs:complexType>

</xs:schema>

# Text boxes

Anemometer(AN)

Relative Humidity(RH)

Barometric Pressure(BP)

Salinity(SA)

Water Temperature(WT)

Air Temperature(AT)

Horizontal visibility(HV)

Wave spectra(WS)

Ocean current(CR)

Radiation(RD)

Precipitation Gauge(PG)

Head recorder

(HR)